## Slide 1: FIREFIGHTING ROBOT
TEAM 14
Amitkumar Patil
Jayanta Das

## Slide 2: Functional requirements
Fire fighting bot should know the path to lift from its parking place.
Lift controller bot should be able to move the lift to the commanded floor.
Fire fighting bot should be able to find its path to the room on fire.
PC (Master controller) should be able to communicate the room no on fire to bot (fire fighting ), the floor no which is on fire to bot (lift controller bot) & coordinate the movements of both the bots.

## Slide 3: Functional requirements
Every room has a fire sensor and there is a mapping between (floor no, room no) and sensor no.
The (floor no, room no) which is on fire has to be communicated to PC (Master controller).
Due to difficulties in construction fire sensor mapping hardware & interfacing it with PC, the above two requirements have been abstracted to
  The (floor no, room no) is read from user on PC.
Once the robot reaches the room which is on fire, it is assumed that fire has been extinguished.

## Slide 4: Risk plan
Synchronization (the movements of fire fighting bot and lift controller).
Stability of the structure, alignment with lift structure.
  Mechanism used for driving the lift (pulley based approach or screw guage approach.

## Slide 5: What we implemented successfully?
Firefighting bot is fully autonomous, it can navigate to any room and come back to starting point or the specified point in the floor.
Necessary API’s (for navigating the floor map) which can be reused in other similar projects.
Basic system of lift mechanism driven by dc motor and controlled by another bot, along with API’s for controlling the lift direction and speed through zigbee communication.

## Slide 6: Things we could not complete
Automating the lift driving mechanism (absence of sensors which tell the lift controlling bot when to stop).

## Slide 7: Test data
Test data consists of (floor no, room no) read from user.
In case multiple rooms or floors are on fire, the test data consists of pairs of (floor no, room no).
Ex:-
  (2,3) – 2nd floor 3rd room has fire.
  (2,3),(4,3),(1,2)